## Slide 1
RISC-V Microcontroller
Developed by Wei-Feng Huang, DICLAB, NCKU
Notes: 老師，各位同學好

## Slide 2: Microcontroller Selection
E203
  RV32IM ISA with interrupt and exception support
  Developed by Nuclei System Technology (China)
  FreeRTOS support available
MicroBlaze V
  Xilinx
  Configurable ISA with interrupt and exception support
  JTAG support available
  FreeRTOS support planned for 2026
  Strong toolchain support (Vivado/Vitis integration, beginner-friendly)
DICLAB’s CPU (developing)
  RV32IMB ISA with interrupt and exception support
  FreeRTOS support targeted

## Slide 3: MicroBlaze V high-end Peripheral
External I/O is FPGA-configurable via GPIO ports.
Onboard switches/LEDs/buttons are also supported.
The right figure shows a Xilinx MicroBlaze V microcontroller reference design example.

## Slide 4: Our Microcontroller (temporary)
MicroBlaze V
Debug
Module
AXI GPIO
AXI Timer
AXI Interrupt
Controller
AXI Interconnect (BUS)
Switch / PWM / LED / RGB LED / Button
AXI UART
JTAG
USB UART
Local Memory
Bus
Data Mem
Inst MEM

## Slide 5: Block Design

## Slide 6: Memory-Mapped I/O vs SFR
Memory-Mapped I/O (MMIO):
  Peripherals are mapped into the memory address space
  Accessed using normal load/store instructions
  Easy to integrate and extend (add new devices by assigning new addresses)
SFR (Special Function Registers) in traditional MCUs (e.g., PIC):
  Peripheral control uses dedicated special registers
  Often requires bank selection / bit-level control
  Less flexible when scaling to more peripherals

## Slide 7: Memory Map in our microcontroller
Each mapped IP provides its own datasheet / product guide.
The document specifies the internal register map (offsets from the base address) and explains how to use each register for configuration and I/O control.

## Slide 8: Memory Architecture
MicroBlaze V
Local Memory
Bus
Data Mem
Inst MEM
CPU internal (MicroBlaze core):
MicroBlaze uses a Harvard-style internal structure, with separate instruction and data paths.
SOC Level:
The overall system looks more like a von Neumann model, because both instructions and data are placed in a single unified memory address space when accessing external memory and memory-mapped peripherals.
Modified Harvard Architecture

## Slide 9: AXI Mapping
Although each peripheral is mapped to a memory address range, this address region does not correspond to physical RAM.
Instead, AXI address decoding and routing logic forwards these transactions to the target peripheral’s register interface (MMIO).

## Slide 10: Resource Utilization
=1.6 * LUT

## Slide 11: Tool Chain
Vivado for FPGA Design (RTL → Bitstream)
Vitis for Software Development (C/C++ → ELF)

## Slide 12: Design Flow

## Slide 13: Program to FPGA and Debug - XSDB (via JTAG)
XSDB (Xilinx System Debugger) communicates with the target board through JTAG (IEEE 1149.1), a standard interface for device programming and hardware debugging.
It uses the MicroBlaze Debug Module (MDM) to halt/reset the CPU and access system memory.
XSDB then downloads the .elf sections (e.g. .text, .data) into on-chip BRAM according to the ELF memory map.
Finally, XSDB sets the program entry point (PC) and starts CPU execution.

## Slide 14: Software Template
Dhystone
Peripheral Test
UART Test
Monte Carlo
Interrupt Service Routine
MicroBlaze V (single-core) measured 0.522 DMIPS/MHz.
Cortex-A9 (dual-core, hard-core) is commonly reported around ~2.5 DMIPS/MHz per core, but in some practical cases it can drop to ~1.0 DMIPS/MHz depending on memory/cache and system configuration.

## Slide 15: Ripes

## Slide 16: Ripes

## Slide 17: Issues to Address
Full Assembly Boot Chain in Vitis (How to Implement)
  start.S : reset entry + stack + jump
  main.S : your main logic (or C main if mixed mode)
  lscript.ld : defines memory regions & entry address
FPGA Board Selection
  Spartan-series without DDR FPGA boards
  Xilinx part number ≤ 35
Cmod S7
Cmod A7